## Slide 1
CYBERSECURITY TRAINING SERIES
Networking Refresher
Network Fundamentals for Cybersecurity
A refresher on core networking concepts every cybersecurity practitioner must know
Notes: Welcome the audience. Introduce this as a networking refresher session aimed at college students, freshers, and cybersecurity beginners. Explain that strong networking fundamentals are the foundation for every cybersecurity skill — you can't defend, attack, or monitor a network you don't understand. Mention the session will run 60-90 minutes and cover network types, devices, addressing, protocols, and hands-on troubleshooting commands.

## Slide 2
SESSION ROADMAP
Agenda
1
What is Networking?
2
Why Networking?
3
Network Types
4
Network Topologies
5
Data Transmission (Casting)
6
Network Devices
7
IP Addressing
8
MAC Addressing
9
IPv4 vs IPv6
10
Public vs Private IP
11
Static vs Dynamic IP
12
Protocol Overview
13
Common Network Protocols
14
Remote Management Protocols
15
Troubleshooting Commands
16
Real-World Network Architecture
17
Summary
18
Quiz
02
NETWORKING REFRESHER
Notes: Walk through the 18 topics we'll cover today. Group them mentally into four buckets: foundations (what/why/types/topologies), addressing (IP/MAC), protocols (overview, common protocols, remote management), and practical skills (troubleshooting commands, real-world architecture, quiz). This helps students see the session has a logical progression rather than a random list.

## Slide 3
FOUNDATIONS
What is Networking?
Networking is the practice of connecting two or more computing devices so they can communicate and share data, resources, and services. Every time you send a message, stream a video, or browse a website, devices are exchanging small units of data called packets across a network — often the largest network of all: the Internet.
PC A
PC B
SWITCH
data packets →
REAL-WORLD EXAMPLE When you send a WhatsApp message, your phone breaks it into packets, sends them over Wi-Fi/mobile data to WhatsApp's servers, which route them across the Internet to your friend's phone — all in milliseconds.
KEY TAKEAWAY Networking = devices exchanging data through defined rules, over cables or radio waves, so information can travel anywhere.
03
NETWORKING REFRESHER
Notes: Define networking simply: connecting devices so they can talk to each other. Use the switch diagram to show two PCs exchanging packets through an intermediate device. Reinforce with the WhatsApp example — something every student uses daily. Teaching tip: ask the class to trace what happens, step by step, when they send a text message, to get them thinking in terms of data flow before diving into formal terms.

## Slide 4
FOUNDATIONS
Why Networking?
A
Resource Sharing
Share printers, storage, and files across devices
B
Communication
Email, chat, and video calls in real time
C
Internet Access
Shared gateway to the global web
D
Collaboration
Multiple users work on shared documents/apps
E
Centralized Mgmt.
Administer users, policies & updates from one place
F
Security
Apply firewalls & access controls network-wide
G
Cost Saving
One resource serves many users, cutting expenses
04
NETWORKING REFRESHER
Notes: Go through each benefit quickly with a concrete classroom or office example: resource sharing (one printer for a whole lab), communication (Slack/Teams), internet access (shared router), collaboration (Google Docs), centralized management (IT pushing an update to every PC at once), security (a single firewall protecting the whole office), cost saving (renting one server instead of buying ten). Emphasize that these benefits are exactly why organizations invest heavily in network infrastructure — and why securing that infrastructure matters.

## Slide 5
FOUNDATIONS
Types of Networks
Type | Coverage | Speed | Owner | Example
PAN | ~10 m | Low | Individual | Bluetooth earbuds
LAN | Building/Campus | Very High | Organization | Office/School network
CAN | Multiple buildings | High | Institution | University campus
MAN | City-wide | High | ISP/Municipality | City cable network
WAN | Country/Global | Moderate | Telecom/ISP | The Internet backbone
SAN | Data center | Very High | Organization | Storage array network
VPN | Virtual / Global | Depends | User/Org | Secure remote work
Internet | Global | Variable | Distributed | Worldwide network of networks
05
NETWORKING REFRESHER
Notes: Compare each network type by scale, starting from the smallest (PAN — your own body-worn devices) up to the largest (the Internet, a network of networks). Point out that LAN is what most students interact with daily at home/school, while WAN describes how LANs are stitched together across distances. Highlight VPN separately: it's not defined by physical distance but by creating a secure, encrypted tunnel over existing infrastructure — very relevant for cybersecurity.

## Slide 6
FOUNDATIONS
Network Topologies
Bus
+ Simple, cheap cabling − One break stops all
Small labs, legacy setups
Star
+ Easy to manage & isolate faults − Central hub is a single point of failure
Home & office LANs
Ring
+ Even data flow, no collisions − One failure can break the loop
Legacy token-ring/MANs
Mesh
+ Highly redundant & reliable − Expensive, complex cabling
Backbone/military networks
Tree
+ Scalable, hierarchical − Depends heavily on root node
Large campus networks
Hybrid
+ Flexible, combines strengths − Complex to design & maintain
Enterprise networks
06
NETWORKING REFRESHER
Notes: Topology describes the physical/logical layout of how devices connect. Walk through each diagram: bus (a single shared backbone cable), star (everything through a central hub/switch — today's most common LAN topology), ring (data passes device to device in a loop), mesh (every node connects to every other — maximum redundancy, used where uptime is critical), tree (hierarchical, star networks joined together), and hybrid (a real-world mix). Ask students to identify which topology their home Wi-Fi router creates (star).

## Slide 7
FOUNDATIONS
Data Transmission (Casting)
Unicast
One sender → one receiver
EXAMPLE Loading a single website page
Broadcast
One sender → all devices on the network
EXAMPLE ARP request finding a MAC address
Multicast
One sender → a specific group
EXAMPLE IPTV / video conference stream
Anycast
nearest
One sender → nearest of several receivers
EXAMPLE DNS root servers, CDNs
07
NETWORKING REFRESHER
Notes: Casting describes how data is addressed to one or many recipients. Unicast is the most common (point-to-point, like loading a webpage). Broadcast sends to every device on the local network segment — necessary but noisy, and often restricted at the router. Multicast targets a defined group, efficient for streaming to many subscribers at once. Anycast routes traffic to the nearest/best server among several sharing the same address — this is how global DNS and CDNs achieve low latency. Ask students which type their video call software probably uses (multicast/unicast mix depending on platform).

## Slide 8
FOUNDATIONS
Network Devices (Part 1)
HUB
Hub
OSI Layer: 1 (Physical)
Broadcasts incoming data to every connected port — no intelligence.
e.g. Legacy Ethernet hub
SW
Switch
OSI Layer: 2 (Data Link)
Forwards data only to the intended device using MAC addresses.
e.g. Cisco Catalyst switch
RT
Router
OSI Layer: 3 (Network)
Connects different networks and directs traffic using IP addresses.
e.g. Home Wi-Fi router
RP
Repeater
OSI Layer: 1 (Physical)
Regenerates and amplifies weak signals over long distances.
e.g. Wi-Fi range extender
BR
Bridge
OSI Layer: 2 (Data Link)
Joins two network segments and filters traffic between them.
e.g. Wireless bridge
GW
Gateway
OSI Layer: All (1-7)
Translates between two different network protocols/architectures.
e.g. VoIP gateway
08
NETWORKING REFRESHER
Notes: Introduce devices in order of intelligence: hubs are 'dumb' broadcasters, switches learn MAC addresses to forward traffic intelligently within a LAN, routers connect separate networks together using IP addresses (this is the device that gives you Internet access at home). Repeaters and bridges extend and segment networks, while gateways translate between completely different protocol stacks — e.g. connecting a VoIP phone system to the regular telephone network. Tie each device to its OSI layer to reinforce that concept for later.

## Slide 9
FOUNDATIONS
Network Devices (Part 2)
FW
Firewall
OSI Layer: 3-7
Filters traffic based on security rules to block unauthorized access.
e.g. pfSense, Windows Firewall
AP
Access Point
OSI Layer: 1-2
Extends a wired network by broadcasting a Wi-Fi signal.
e.g. Ubiquiti UniFi AP
MD
Modem
OSI Layer: 1 (Physical)
Converts digital signals to analog (and back) for ISP lines.
e.g. Cable/DSL modem
LB
Load Balancer
OSI Layer: 4-7
Distributes traffic across multiple servers for reliability.
e.g. NGINX, F5 Big-IP
IDS
IDS
OSI Layer: 3-7
Monitors traffic and alerts on suspicious/malicious activity.
e.g. Snort, Suricata
IPS
IPS
OSI Layer: 3-7
Detects AND actively blocks malicious traffic in real time.
e.g. Cisco Firepower
09
NETWORKING REFRESHER
Notes: This second group leans security-relevant: firewalls enforce rule-based access control; access points and modems handle the 'last mile' connectivity; load balancers keep services available under heavy traffic. Spend extra time on IDS vs IPS since this distinction commonly appears in interviews — an IDS is passive (detect and alert only), while an IPS is active (detect and block). Ask students: 'would you rather deploy an IDS or IPS on a network segment with mission-critical, latency-sensitive traffic?' to spark discussion on trade-offs.

## Slide 10
ADDRESSING
IP Addressing
IP Address
Unique logical address identifying a device on a network
Host
Any device connected to the network (PC, printer, phone)
Network ID
Portion of the IP identifying which network a host belongs to
Subnet
A smaller, logically segmented section of a larger network
Default Gateway
The router address a device uses to reach other networks
CIDR
Notation (e.g. /24) expressing the subnet mask length
Private / Public IP
Internal-only address vs. globally routable address
Loopback
127.0.0.1 — address a device uses to refer to itself
APIPA
169.254.x.x — auto-assigned when no DHCP server responds
CIDR BREAKDOWN — 192.168.1.10 / 24
192.168.1
.10
NETWORK ID
HOST ID
/24 = first 24 bits (3 octets) identify the network; the remaining 8 bits identify the host on that network.
KEY TAKEAWAY An IP address has two parts — Network ID and Host ID — and CIDR notation tells you exactly where the split happens.
10
NETWORKING REFRESHER
Notes: Cover the core vocabulary first: IP address, host, network ID, subnet, gateway. Then use the CIDR diagram to make the abstract concrete — a /24 means the first three octets are the network portion (shared by every device on that LAN) and the last octet is the unique host portion. Mention private vs public IP and loopback/APIPA briefly here; they'll be revisited in the Address Comparisons slide. Teaching tip: ask a student to run ipconfig/ifconfig on their own laptop and identify their IP's network vs host portion live.

## Slide 11
ADDRESSING
IPv4 vs IPv6
Feature | IPv4 | IPv6
Address Size | 32-bit | 128-bit
Address Space | ~4.3 billion addresses | 340 undecillion addresses
Format | Decimal, dotted (192.168.1.1) | Hexadecimal, colon (2001:db8::1)
Header | Complex, variable length | Simplified, fixed length
Security | Optional (IPSec add-on) | Built-in (IPSec mandatory)
Broadcast | Supported | Not used — multicast/anycast instead
Configuration | Manual or DHCP | Supports auto-configuration (SLAAC)
Example | 203.0.113.5 | 2001:0db8:85a3::8a2e:0370:7334
KEY TAKEAWAY IPv6 was created because the world ran out of IPv4 addresses — but IPv4 remains dominant, so cybersecurity pros must know both.
11
NETWORKING REFRESHER
Notes: IPv4's 32-bit space provides about 4.3 billion addresses — not enough for a planet full of phones, laptops, and IoT devices, which is why IPv6's 128-bit space (a virtually inexhaustible number) was introduced. Point out the format difference (dotted decimal vs colon hex) since misreading an IPv6 address is a common beginner mistake. Highlight that IPv6 makes IPSec encryption mandatory, which is a meaningful security upgrade. In practice, most networks today run 'dual-stack' — both IPv4 and IPv6 simultaneously.

## Slide 12
ADDRESSING
MAC Address
A MAC (Media Access Control) address is a physical, hardware-burned-in address assigned to a device's Network Interface Card (NIC) by its manufacturer. Unlike an IP address, a MAC address doesn't change when a device moves to a different network — it uniquely identifies the physical hardware itself, and operates at Layer 2 (Data Link) of the OSI model.
NIC
Network Interface Card
Burned into hardware at the factory
00:1A:2B
3C:4D:5E
OUI — MANUFACTURER ID
DEVICE-SPECIFIC ID
KEY TAKEAWAY MAC = 'who' (physical hardware), IP = 'where' (logical location on a network) — both are needed to deliver data correctly.
12
NETWORKING REFRESHER
Notes: Emphasize the physical vs logical distinction: MAC addresses are fixed to hardware (like a serial number), while IP addresses can change depending on which network you join. Show the format: six pairs of hex digits, where the first three pairs (the OUI) identify the manufacturer, and the last three uniquely identify the device. Mention that MAC addresses operate at Layer 2 and are how switches forward frames within a LAN, whereas IP (Layer 3) is how routers forward packets between networks.

## Slide 13
ADDRESSING
Address Comparisons
IPv4
IPv6
32-bit, decimal
128-bit, hex
Public IP
Private IP
Globally routable, unique
Local-only, reusable (192.168.x.x)
Static IP
Dynamic IP
Fixed, manually set
Assigned automatically by DHCP
Logical Addr.
Physical Addr.
IP — changes per network
MAC — fixed to hardware
MAC
IP
Layer 2, hardware ID
Layer 3, network location
Gateway
DNS
Router to leave the network
Server that resolves names to IPs
13
NETWORKING REFRESHER
Notes: This slide is a rapid-fire recap contrasting six commonly confused address pairs. Go through each card and ask the class to state the key difference before revealing it. Pay special attention to Gateway vs DNS, since students often conflate them — the gateway is the door out of your network, while DNS is the phonebook that turns names like google.com into IP addresses. This is a good checkpoint slide before moving into protocols.

## Slide 14
PROTOCOLS
Protocol Overview & the TCP/IP Stack
A protocol is a defined set of rules that governs how devices communicate — determining format, timing, sequencing, and error handling for data exchange. Without shared protocols, devices from different vendors couldn't understand each other.
Application
HTTP, HTTPS, DNS, FTP, SMTP
How apps talk — the data you see (web pages, emails)
Transport
TCP, UDP
End-to-end delivery — reliable (TCP) or fast (UDP)
Internet
IP, ICMP, ARP
Logical addressing & routing between networks
Network Access
Ethernet, Wi-Fi
Physical transmission over cables or radio waves
↑ Data flows down this stack when sending, and up when receiving ↓
14
NETWORKING REFRESHER
Notes: Introduce the four-layer TCP/IP model (a practical simplification of the seven-layer OSI model). Explain the encapsulation concept: when sending data, it moves down the stack, with each layer adding its own header, then travels across the wire, and on the receiving end moves back up the stack being unwrapped at each layer. Give one protocol example per layer and connect it to something familiar — HTTPS at Application when browsing a secure site, TCP at Transport ensuring your file download arrives complete, IP at Internet routing packets globally, Ethernet/Wi-Fi at Network Access as the physical medium.

## Slide 15
PROTOCOLS
Common Network Protocols (Part 1)
Protocol | Port | Type | Purpose | Real-World Example
HTTP | 80 | TCP | Transfers web pages (unencrypted) | Browsing an old blog site
HTTPS | 443 | TCP | Transfers web pages, encrypted with TLS | Online banking login
FTP | 20/21 | TCP | Transfers files between client & server | Uploading a website's files
SFTP | 22 | TCP | Secure, encrypted file transfer over SSH | Sending confidential reports
SSH | 22 | TCP | Encrypted remote login & command execution | Administering a Linux server
Telnet | 23 | TCP | Unencrypted remote login (legacy) | Old router/switch console access
SMTP | 25 | TCP | Sends outgoing email | Gmail sending your message
POP3 | 110 | TCP | Downloads email, then removes from server | Legacy desktop mail clients
IMAP | 143 | TCP | Syncs email across multiple devices | Checking email on phone & laptop
15
NETWORKING REFRESHER
Notes: This first batch covers web, file transfer, remote access, and email protocols. Draw the HTTP vs HTTPS distinction clearly — the 'S' means TLS encryption, and it's the single most important security upgrade a student can recognize in a browser address bar. Contrast FTP/Telnet (plaintext, legacy, insecure) against SFTP/SSH (encrypted, modern replacements) — this pairing is a great entry point into why cybersecurity professionals care about protocol choice. Briefly note POP3 vs IMAP: POP3 downloads and deletes from the server, IMAP keeps everything synced across devices.

## Slide 16
PROTOCOLS
Common Network Protocols (Part 2)
Protocol | Port | Type | Purpose | Real-World Example
DNS | 53 | TCP/UDP | Resolves domain names to IP addresses | Typing google.com in a browser
DHCP | 67/68 | UDP | Automatically assigns IP addresses | Your phone joining Wi-Fi
SNMP | 161/162 | UDP | Monitors & manages network devices | Dashboard showing router health
LDAP | 389 | TCP/UDP | Accesses & manages directory services | Corporate user login (Active Directory)
NTP | 123 | UDP | Synchronizes device clocks | Server time staying accurate
SMB | 445 | TCP | Shares files/printers on a LAN | Accessing a shared office drive
RDP | 3389 | TCP | Remote graphical desktop access | Connecting to a work PC from home
ICMP | — | IP-based | Diagnostics & error reporting | The ping command
ARP | — | L2 broadcast | Maps an IP address to a MAC address | Device finding its LAN neighbor
16
NETWORKING REFRESHER
Notes: This set focuses on infrastructure and internal-network protocols. DNS and DHCP are the two protocols that make 'plug and play' networking possible — DHCP hands out an IP automatically, DNS lets you use names instead of memorizing numbers. SNMP and LDAP are common enterprise/monitoring protocols worth knowing for IT and security roles. Point out ICMP and ARP don't use ports the way TCP/UDP protocols do — ICMP rides directly on IP (that's what ping uses), and ARP operates at Layer 2 to map IPs to MAC addresses on the local segment.

## Slide 17
PROTOCOLS
Remote Management Protocols
Protocol | Port | Interface | Security Level
SSH | 22 | Command-line | 
Telnet | 23 | Command-line | 
RDP | 3389 | Full graphical desktop | 
VNC | 5900 | Full graphical desktop | 
WinRM | 5985/5986 | Windows remote management | 
Encrypted
Plaintext
Encrypted (TLS optional)
Varies (often unencrypted)
Encrypted (HTTPS mode)
KEY TAKEAWAY Prefer SSH, RDP with NLA, or WinRM over HTTPS — avoid Telnet and unauthenticated VNC, which send credentials in plaintext.
17
NETWORKING REFRESHER
Notes: Remote management protocols let administrators control devices from anywhere. Stress the security contrast: SSH encrypts everything (the secure replacement for Telnet, which sends credentials and commands in plaintext — a classic finding in penetration tests). RDP is Windows' native remote desktop protocol and is reasonably secure when Network Level Authentication is enabled, but is also a very common ransomware entry point when exposed directly to the Internet. VNC's security depends heavily on configuration. WinRM is used heavily in Windows enterprise administration and automation (e.g. PowerShell remoting).

## Slide 18
PRACTICAL SKILLS
Network Troubleshooting Commands
ping
Tests reachability & round-trip time to a host
ipconfig / ifconfig
Shows local IP, subnet, and gateway (Win/Linux)
tracert / traceroute
Shows the path (hops) packets take to a destination
netstat
Lists active connections & listening ports
arp
Displays the local IP-to-MAC address cache
route
Views/edits the local routing table
nslookup / dig
Queries DNS to resolve a domain to an IP
hostname
Displays the device's network host name
curl
Sends HTTP requests directly from the command line
18
NETWORKING REFRESHER
Notes: These are the day-one diagnostic commands every network and security professional reaches for. Group them by purpose while presenting: connectivity testing (ping, tracert/traceroute), local configuration (ipconfig/ifconfig, hostname), active connections (netstat, arp, route), and DNS/HTTP tools (nslookup/dig, curl). Live-demo at least ping and tracert/traceroute if possible — seeing the hop-by-hop path in traceroute is often the 'aha' moment that makes routing concepts click for beginners.

## Slide 19
PRACTICAL SKILLS
Real-World Office Network Architecture
Internet
Firewall
Router
Core Switch
Access Switch
Servers
Data & app hosting
PCs
Wired workstations
WiFi AP
Wireless coverage
Printers
Shared devices
Laptops
Mobile Devices
KEY TAKEAWAY Traffic funnels from the Internet through a firewall (security checkpoint) and router before fanning out to switches, servers, and endpoints.
19
NETWORKING REFRESHER
Notes: Walk through the flow left to right: the Internet connection first hits the firewall — the organization's primary security checkpoint, filtering traffic before anything else touches the internal network. It then passes through the router (or a combined firewall/router appliance in smaller offices), down to the core switch (the network backbone), and out to access switches on each floor/department. From there, traffic reaches servers, wired PCs, wireless access points (which serve laptops and mobile devices), and printers. This is the architecture most students will encounter in their first IT or security job — ask them to identify where they'd place a monitoring/IDS sensor for maximum visibility.

## Slide 20
RECAP
Quick Revision
Types
Devices
Protocols
IP Addressing
MAC Addressing
Topology
Commands
NETWORKING
20
NETWORKING REFRESHER
Notes: Use this mind map as an active-recall exercise rather than just a summary — for each branch, ask the class to name one fact before you reveal it. Types (from PAN to the Internet), Topology (star, mesh, etc.), Devices (routers, switches, firewalls...), IP and MAC Addressing (logical vs physical), Protocols (the rules governing communication), and Commands (the diagnostic toolkit). If everything on this map feels familiar, the class is ready for the quiz.

## Slide 21
CHECK YOUR UNDERSTANDING
Quiz
Q1. Which protocol uses Port 22?
A FTP
B SSH
C DNS
D HTTP
Q2. Which device operates primarily at Layer 3?
A Switch
B Hub
C Router
D Repeater
Q3. What does CIDR /24 indicate?
A 24 hosts
B 24-bit network mask
C 24 subnets
D Port 24
Q4. Which topology connects every node to every other node?
A Star
B Bus
C Mesh
D Ring
Q5. Which address type is 00:1A:2B:3C:4D:5E?
A IP
B MAC
C Gateway
D Subnet
Q6. Which casting type sends to the nearest of several servers?
A Unicast
B Multicast
C Broadcast
D Anycast
Answer key: see speaker notes.
21
NETWORKING REFRESHER
Notes: Run this as an interactive check-for-understanding — read each question aloud and have students answer before revealing the correct option verbally. No answers are shown on the slide, so it's safe to project as-is. Use wrong answers as teaching moments: e.g. for Q2, discuss why a hub (Layer 1) and switch (Layer 2) are common wrong picks versus the router's Layer 3 role. ANSWER KEY — Q1: B (SSH) | Q2: C (Router) | Q3: B (24-bit network mask) | Q4: C (Mesh) | Q5: B (MAC) | Q6: D (Anycast)

## Slide 22
RECAP
Summary
1
Networking Basics
2
Network Types
3
Network Devices
4
Topologies
5
IP & MAC Addressing
6
Protocols
7
Troubleshooting Commands
8
Cybersecurity Importance
KEY TAKEAWAY Master these eight pillars and you have the foundation to secure, monitor, and troubleshoot any network with confidence.
22
NETWORKING REFRESHER
Notes: Close the technical content with a full-circle recap of everything covered: basics of what/why networking exists, the types and topologies that structure a network, the devices that build it, the addressing schemes (IP and MAC) that identify devices on it, the protocols that govern communication, the commands used to troubleshoot it, and — most importantly for this audience — why all of this matters for cybersecurity. Every attack, defense, and investigation technique builds on these fundamentals.

## Slide 23
Thank You
Questions?
Networking Refresher — Cybersecurity Training Series
Notes: Thank the audience for their attention and open the floor for questions. Encourage students to revisit the troubleshooting commands and protocol port numbers on their own, since hands-on repetition is what makes these fundamentals stick. If time allows, invite them to run through the quiz once more or try the commands from Slide 18 on their own machines.